## Slide 1
Discrete I/O Fundamentals
Target platform: EVKB i.MX RT1050
Focus on avionics-style discretes
Emphasis on robust, deterministic engineering choices

## Slide 2
What “Discrete I/O” Means in Avionics
A discrete is a binary electrical signal (asserted/de-asserted)
Used to announce aircraft states: WOW, FLT/GRD, FIRE DETECT, DOOR CLOSED, APU READY
Software interfaces via GPIO pins

## Slide 3
GPIO Capabilities for Discretes
Configurable as input or output
Internal pull-ups/pull-downs
Schmitt trigger for noise rejection
Open-drain mode, drive strength, slew rate
Goal: reliable logic levels + noise immunity

## Slide 4
i.MX RT1050 Pin Mux & Pad Configuration
Each pad routed through a pin mux
Select GPIO function first
Configure pad electrical characteristics: pulls, slew, drive, hysteresis
Ensures reliable, noise-tolerant logic

## Slide 5
Safety-Critical Expectations
Deterministic behavior required
BIT (Built-In Test) for diagnosability
EMI/EMC and ESD robustness (DO-160)
DAL processes (DO-178C / DO-254) assume disciplined discrete design

## Slide 6
Key Terminology (1 of 2)
GPIO: configurable digital pin
VIH / VIL: input thresholds
VOH / VOL: output voltage guarantees
Drive strength: sourcing/sinking capability
Slew rate: edge speed (affects EMI)

## Slide 7
Key Terminology (2 of 2)
Schmitt trigger: hysteresis for noise rejection
Pull-up / pull-down: define default state
Push-pull: active high + low drive
Open-drain: only pulls low; pull-up defines high
Debounce: removes chatter/spikes
Wired-OR / wired-AND: shared open-drain lines

## Slide 8
Electrical Characteristics: Logic Levels
EVKB I/O domain: 3.3 V LVCMOS
Thresholds often fractions of VDDIO
Never exceed supply rails
Respect absolute maximum ratings

## Slide 9
Electrical Characteristics: Inputs
Floating inputs are unsafe
Use pull-up for active-low, pull-down for active-high
Schmitt trigger recommended for external signals
Glitch filtering via software or hardware

## Slide 10
Pull-Ups / Pull-Downs (1 of 2)
Define default state
Provide leakage path for EMI immunity
Assist logic-family interfacing
Required for open-drain outputs

## Slide 11
Pull-Ups / Pull-Downs (2 of 2)
Improve effective drive in some cases
Unused CMOS inputs must not float
Biasing helps long-line stability
Preset bus idle state (e.g., I²C)
Improve noise tolerance

## Slide 12
Outputs: Push-Pull vs Open-Drain
Push-pull: drives high and low
Open-drain: pulls low; pull-up defines high
Useful for shared lines and level shifting
Real behavior includes line capacitance

## Slide 13
Drive Strength & Slew Rate
Use lowest drive strength that meets timing
Slow edges reduce EMI and ringing
Fast edges increase emissions and susceptibility

## Slide 14
Protection & Aircraft Interfacing
Aircraft discretes often 28 V
Never connect directly to MCU pins
Use dividers, TVS, RC filters, isolation
Outputs via transistor/MOSFET stages
Add EMI/ESD components per DO-160

## Slide 15
EVKB SDK Building Blocks
Pin mux/pad control via IOMUXC
GPIO driver for init/read/write/interrupts
Board helpers for clocks and console
Use SDK macros for LED/button mapping

## Slide 16
Workflow: Requirements → Pad Config → Logic
Start with requirement statement
Choose hardware strategy (pulls, hysteresis, debounce)
Initialize pin mux and pad config
Configure GPIO direction/interrupts
Implement read/write behavior

## Slide 17
Avionics Use Case: WOW with Diagnostics
Input via isolated interface
Filter bounce/spikes; vote samples
Timestamp edges for maintenance
Output FLT/GRD via open-drain
BIT for stuck-at faults
Record raw + filtered states

## Slide 18
Hands-On Labs Overview
Bare-metal project with board init
Use SDK macros for portability
Progression: Skeleton → Output → Input+Debounce → Voting+Timestamp → Pad Audit

## Slide 19
Lab 0: Project Skeleton
Initialize pins, clocks, console
Print startup banner
Idle loop for observability

## Slide 20
Lab 1: Output Lab
Configure LED as output
Blink/toggle at known rate
Push-pull appropriate for 3.3 V
Adjust drive/slew if EMI observed

## Slide 21
Lab 2: Input Lab (SW8)
Configure SW8 with edge interrupts
Enable pull-up + hysteresis
Deterministic debounce
Toggle LED on stable press

## Slide 22
Lab 3: Toward WOW
Timestamp edges
Convert raw active-low to logical state
Majority vote window (e.g., 3/5)
Print edge time + voted truth
Reflect truth on LED

## Slide 23
Lab 4: Pad Settings Audit
Confirm mux selection
Inputs: pulls + hysteresis
Outputs: slow slew + modest drive
Use open-drain for shared discretes
Track pad config across SDK versions

## Slide 24
Avionics Scenarios to Simulate
WOW with transient spikes
Wired-OR FLT/GRD line
Stuck-at BIT detection
EMI tradeoff: drive/slew comparison

## Slide 25
Best Practices (Hardware)
Match electrical domains
Fail-safe states via pulls/output type
Enable hysteresis for external discretes
Avoid fighting strong external pulls
Reduce EMI with low drive/slow slew

## Slide 26
Best Practices (Software + Process)
Deterministic debounce
BIT for stuck-at/open circuit
Keep ISRs short
Document pad/bank/rail mapping
Maintain traceability

## Slide 27
Assessment Checklist
Asserted polarity + fail-safe documented
Pad configs correct
Debounce rationale stated
BIT covers stuck-at + open
Edge timestamps logged
EMI/ESD robustness considered

## Slide 28
ARINC 429 Note
ARINC 429 is differential, not a discrete
GPIO used for enables, health lines, label-present signals
Discrete concepts apply to companion lines

## Slide 29
Implementation Guidance
Prefer SDK board macros
Use MCUXpresso Pins Tool
Explicitly set pulls, hysteresis, drive, slew, open-drain
Keep pin config files under revision control