## Slide 1
Discrete I/O Fundamentals
GPIO configuration and electrical characteristics
Target platform: EVKB i.MX RT1050
Focus: avionics style “discretes” and robust engineering choices
1
Notes: Sources: Internal content derived from the uploaded “Discrete IO Fundamentals.docx”. No code snippets included.

## Slide 2
What “Discrete I/O” Means in Avionics
A discrete is a binary signal: an electrical line that is asserted (true) or de asserted (false)
Discretes announce aircraft states like WOW, FLT/GRD, FIRE DETECT, DOOR CLOSED, APU READY
Software interfaces to discretes through GPIO pins
2
Notes: Sources: Internal content derived from the uploaded “Discrete IO Fundamentals.docx”. No code snippets included.

## Slide 3
GPIO Capabilities You Use for Discretes
Configure GPIO as input or output
Internal pull ups and pull downs to define a default state
Schmitt trigger (hysteresis) for noise rejection
Open drain mode, drive strength, and slew rate control
Goal: reliable logic levels and noise immunity
3
Notes: Sources: Internal content derived from the uploaded “Discrete IO Fundamentals.docx”. No code snippets included.

## Slide 4
i.MX RT1050 Pin Mux and Pad Configuration
Each physical pad is routed through a pin mux to a chosen peripheral function (GPIO, UART, SPI, etc.)
First select GPIO in the mux
Then configure pad electrical characteristics (pulls, slew, drive, hysteresis)
Rationale: logic must be reliable, noise tolerant, and compatible with surrounding hardware
4
Notes: Sources: Internal content derived from the uploaded “Discrete IO Fundamentals.docx”. No code snippets included.

## Slide 5
Safety Critical Expectations Around Discretes
Determinism is expected in safety critical avionics implementations
Diagnosability via BIT (Built In Test) is a typical requirement
Tolerance to EMI/EMC and ESD is expected (e.g., DO 160)
DAL software (DO 178C) and hardware (DO 254) processes assume disciplined discrete engineering
5
Notes: Sources: Internal content derived from the uploaded “Discrete IO Fundamentals.docx”. No code snippets included.

## Slide 6
Key Terminology (1 of 2)
GPIO: configurable digital pin used as binary input or output
VIH / VIL: input high/low thresholds (recognized as logic 1 / logic 0)
VOH / VOL: guaranteed output high/low voltages under load
Drive strength: sourcing and sinking capability while maintaining valid logic levels
Slew rate: edge speed (slower edges generally reduce EMI)
6
Notes: Sources: Internal content derived from the uploaded “Discrete IO Fundamentals.docx”. No code snippets included.

## Slide 7
Key Terminology (2 of 2)
Schmitt trigger (hysteresis): separate rising/falling thresholds to reject noise and slow edges
Pull up / pull down: weak resistors to rails that prevent floating and define defaults
Push pull: output can actively drive both high and low
Open drain: output can only pull low; external or internal pull up defines high level
Debounce: filtering to remove mechanical chatter and narrow spikes
Wired OR / wired AND: multiple open drain outputs share a line; any device pulling low dominates
7
Notes: Sources: Internal content derived from the uploaded “Discrete IO Fundamentals.docx”. No code snippets included.

## Slide 8
Electrical Characteristics: Logic Levels and Supplies
EVKB user I/O domain is 3.3 V (LVCMOS)
Thresholds are often expressed as fractions of VDDIO (confirm in datasheet)
Never drive GPIO above its bank supply or below ground beyond allowed limits
Always respect absolute maximum ratings
8
Notes: Sources: Internal content derived from the uploaded “Discrete IO Fundamentals.docx”. No code snippets included.

## Slide 9
Electrical Characteristics: Inputs
Floating inputs are unsafe and noise sensitive
Use pull up for active low signals and pull down for active high signals
Schmitt trigger is especially valuable for external harnessed signals or RC filtered inputs
Glitch filtering can be done in software (sampling and debounce) or hardware where available
9
Notes: Sources: Internal content derived from the uploaded “Discrete IO Fundamentals.docx”. No code snippets included.

## Slide 10
Pull Up / Pull Down: Why They Exist (1 of 2)
Define a default state so an input does not float
Provide a leakage path that improves immunity to external electromagnetic interference
Help when interfacing logic families (example: raising an otherwise marginal “high” level in some interfacing cases)
Required for open collector or open drain style outputs so the line can return high
10
Notes: Sources: Internal content derived from the uploaded “Discrete IO Fundamentals.docx”. No code snippets included.

## Slide 11
Pull Up / Pull Down: Additional Practical Reasons (2 of 2)
Improve effective drive capability for some pins by providing a defined bias path
Unused CMOS inputs should not be left floating; bias them to a known level to reduce ESD and EMI susceptibility
For longer lines, biasing and impedance planning helps reduce false switching and reflection issues (proper termination strategy still matters)
Preset bus idle state (example: I2C idle high uses pull ups)
Improve noise tolerance by avoiding random levels in high impedance states
11
Notes: Sources: Internal content derived from the uploaded “Discrete IO Fundamentals.docx”. No code snippets included.

## Slide 12
Electrical Characteristics: Outputs (Push Pull vs Open Drain)
Push pull output stage can source or sink current (drive high and low)
Useful for on board logic at the same voltage domain
Open drain outputs pull low via a transistor; a pull up completes the path to logic high
Open drain is useful for shared lines, fail safe wired OR, and level shifting (with correct external circuitry)
Real line behavior also includes capacitance from PCB traces and connected devices (affects edges and rise time)
12
Notes: Sources: Internal content derived from the uploaded “Discrete IO Fundamentals.docx”. No code snippets included.

## Slide 13
Drive Strength and Slew Rate
Use the lowest drive strength and slowest slew rate that still meets timing
Slower edges reduce EMI and ringing
Faster edges can increase emissions and susceptibility issues
13
Notes: Sources: Internal content derived from the uploaded “Discrete IO Fundamentals.docx”. No code snippets included.

## Slide 14
Protection and Aircraft Interfacing Reality
Aircraft discretes may be based on 28 V nominal systems
Never connect aircraft level signals directly to MCU GPIO pins
Use appropriate external interface circuitry: dividers, TVS, RC filters, isolation (optocoupler or digital isolator)
For outputs, use transistor or MOSFET stages (often open drain style) into aircraft discrete networks
Add EMI and ESD components consistent with DO 160 style robustness expectations
14
Notes: Sources: Internal content derived from the uploaded “Discrete IO Fundamentals.docx”. No code snippets included.

## Slide 15
EVKB i.MX RT1050 SDK Building Blocks
Pin mux and pad control via IOMUXC APIs (or tool generated pin initialization)
GPIO driver provides pin init, read, write, and interrupt configuration
Board helpers initialize pins, clocks, and debug console printing
Use the SDK board macros for LED and button mapping rather than hardcoding banks and pins
15
Notes: Sources: Internal content derived from the uploaded “Discrete IO Fundamentals.docx”. No code snippets included.

## Slide 16
Workflow: Requirements → Pad Configuration → GPIO Logic
Start with a requirement statement (example: active low input with debounce + LED output)
Choose hardware strategy: pull up, hysteresis, and debounce plan
Initialize baseline pin mux and pad config (board init or pin tool output)
Configure GPIO direction and interrupts
Implement read and write behavior (polling or ISR plus filtering)
16
Notes: Sources: Internal content derived from the uploaded “Discrete IO Fundamentals.docx”. No code snippets included.

## Slide 17
Avionics Use Case Example: WOW with Diagnostics
Input WOW discrete through an isolated interface
Filter bounce and spikes, then vote samples to determine a robust truth
Timestamp edges for maintenance logging to a central maintenance computer
Output FLT/GRD as an open drain discrete so multiple LRUs can share the line (wired OR)
Power up and periodic BIT detect stuck at faults
Record both raw and filtered states with timestamps
17
Notes: Sources: Internal content derived from the uploaded “Discrete IO Fundamentals.docx”. No code snippets included.

## Slide 18
Hands On Labs Overview (What You Build)
Labs assume a bare metal project with board pin init, clock init, and debug console init
LED and button pins are taken from SDK macros so projects are portable and consistent
Progression: project skeleton → output control → input with interrupt and debounce → voting and timestamping → pad audit
18
Notes: Sources: Internal content derived from the uploaded “Discrete IO Fundamentals.docx”. No code snippets included.

## Slide 19
Lab 0: Project Skeleton (No Code Shown)
Initialize pins, clocks, and debug console
Print a startup banner to prove basic bring up
Run an idle loop to keep the firmware alive and observable
19
Notes: Sources: Internal content derived from the uploaded “Discrete IO Fundamentals.docx”. No code snippets included.

## Slide 20
Lab 1: Output Lab (User LED)
Configure the user LED GPIO as a digital output
Blink or toggle at a known rate
Reasoning: LED is local at 3.3 V so push pull is appropriate
If EMI issues are observed, reduce drive strength and slow slew via pad config
20
Notes: Sources: Internal content derived from the uploaded “Discrete IO Fundamentals.docx”. No code snippets included.

## Slide 21
Lab 2: Input Lab (SW8) with Robustness
Configure SW8 as an input with edge interrupts
Ensure pull up and hysteresis are enabled at the pad level for noise immunity
Implement deterministic debounce (example: resample after a fixed delay)
Provide feedback by toggling the LED when a stable press is detected
21
Notes: Sources: Internal content derived from the uploaded “Discrete IO Fundamentals.docx”. No code snippets included.

## Slide 22
Lab 3: Toward WOW (Timestamp + Voting)
Timestamp each detected edge using a microsecond time base
Convert raw active low input into a logical asserted state
Use a majority vote window (example: 3 of 5) to create a robust truth
Print edge time and voted truth, and reflect truth on LED
22
Notes: Sources: Internal content derived from the uploaded “Discrete IO Fundamentals.docx”. No code snippets included.

## Slide 23
Lab 4: Pad Settings You Must Be Able to Audit
Confirm mux selection matches intended GPIO pad routing
Inputs: enable pull and Schmitt trigger hysteresis (especially external signals)
Outputs: choose slow slew and modest drive unless timing demands otherwise
Use open drain when creating shared aircraft discrete outputs
Maintain awareness of pad configuration values as device and SDK version specifics
23
Notes: Sources: Internal content derived from the uploaded “Discrete IO Fundamentals.docx”. No code snippets included.

## Slide 24
Avionics Grade Scenarios to Simulate
WOW with transient spikes: inject brief pulses and show filtering rejects them
Wired OR FLT/GRD line: two open drain outputs share one pull up line; either can assert low
Stuck at BIT: force stuck low or stuck high and detect at power up or periodically
EMI tradeoff: observe ringing at high toggle rate, then reduce drive and slow slew and compare behavior
24
Notes: Sources: Internal content derived from the uploaded “Discrete IO Fundamentals.docx”. No code snippets included.

## Slide 25
Best Practices (Hardware)
Match electrical domains: never expose 28 V discretes directly to MCU pins
Fail safe states: choose pulls and output types so faults default to the least hazardous meaning
Enable hysteresis for external discretes
Respect pull strengths: avoid fighting strong external pulls with internal ones
Tame EMI using low drive, slow slew, and optional series resistors
25
Notes: Sources: Internal content derived from the uploaded “Discrete IO Fundamentals.docx”. No code snippets included.

## Slide 26
Best Practices (Software + Process)
Debounce deterministically with a stable time base and record raw and filtered state
BIT for stuck at and open circuit; use loopbacks where possible
Keep ISRs short: clear flags first, defer work to main loop or task
Document pad to bank to rail mapping; keep pin configuration under revision control
Maintain traceability: requirements → pad config → code → tests
26
Notes: Sources: Internal content derived from the uploaded “Discrete IO Fundamentals.docx”. No code snippets included.

## Slide 27
Assessment Checklist
Asserted polarity and fail safe state documented
Pad configs set pulls, hysteresis, slew, drive, and open drain where needed
Debounce and filtering rationale stated (example: 5 ms)
BIT covers stuck high, stuck low, and open circuit behaviors
Edge timestamps logged for maintenance support
EMI and ESD robustness considered in design assumptions and lab validation
27
Notes: Sources: Internal content derived from the uploaded “Discrete IO Fundamentals.docx”. No code snippets included.

## Slide 28
Note for Later ARINC 429 Sessions
ARINC 429 is differential and unidirectional, not a discrete
In real systems you still manage enables, health discretes, and label present lines via GPIO
All discrete concepts here apply directly to companion GPIO lines around the ARINC transceiver
28
Notes: Sources: Internal content derived from the uploaded “Discrete IO Fundamentals.docx”. No code snippets included.

## Slide 29
Implementation Guidance
Prefer SDK board macros rather than hardcoding banks and pins
Use the MCUXpresso Pins Tool to generate pin mux and pad configuration
Explicitly include electrical options you require (pulls, hysteresis, drive, slew, open drain)
Keep generated pin configuration files under configuration management
29
Notes: Sources: Internal content derived from the uploaded “Discrete IO Fundamentals.docx”. No code snippets included.